## Slide 1: Pipeline Hazard Detection
Jack Meadows

## Slide 2: Introduction
Read After Write (RAW) Hazards
  An instruction reads from a source before its ready
  Can be solved by forwarding
Load Use Hazard
  Data is not ready when it's needed
  Must stall
  Most common bottleneck
Control Hazard
  Caused by branching
  Wrong instruction fetched
  Pipeline must flush

## Slide 3: Set Up
Modified Assignment 5’s pipeline simulator
Updated hex_inst.txt to create hazards to demonstrate the hazard detection

## Slide 4: Implementation
Hazard Detector Class
  Stores all data for report log including stalls, hazards, and CPI
  Creates the report file
Hazard Detection Section
  Checks if ID reads what EX/MEM/WB writes and logs hazard
  Looks if EX loads an instruction and if ID needs that register
  If so insert a stall cycle

## Slide 5: Demo

## Slide 6: Conclusion
All stalls are from Load-Use hazards not from RAW
The RAW hazards don’t cause any stalls from forwarding
Just a small amount of Load-Use hazards created a large percent of stall cycles